## Slide 1: Robot Action Anticipation for Collaborative Assembly Tasks
Articles Review

## Slide 2: Anticipative interaction primitives for human-robot collaboration
The robot should decide whether to hand over a screw or a plate and which plate;
As the experience with a given user grows, it learns the pattern in which the parts are being assembled;
Use a lookup table containing variations of assembly sequences, previously demonstrated by different users;
Use nearest neighbour sequence in the table that matches the actual sequence of human actions.
Authors: Guilherme Maeda, Aayush Maloo, Marco Ewerton, Rudolf Lioutikov, Jan Peters
Publisher: AAAI Fall Symposium - Technical Report
Year: 2016

## Slide 3: Anticipation in Human-Robot Cooperation: A recurrent neural network approach for multiple action sequences prediction
The robot must predict human actions and intent, and understand human non-verbal cues: gaze and body posture;
Encoder-decoder recurrent neural network topology;
Predicting multiple action sequences;
Aside from the camera, there were wearable sensors to detect gaze.
Authors: Paul Schydlo, Mirko Rakovic, Lorenzo Jamone, José Santos-Victor
Publisher: Proceedings - IEEE International Conference on Robotics and Automation
Year: 2018

## Slide 4: Prediction‐Based Human‐Robot Collaboration in Assembly Tasks Using a Learning from Demonstration Model
Human intention prediction providing the required pieces to the human worker;
ConvLSTM to predict intention and CNN to recognize the part needed;
There are speed limits on the robot, it normally stays out of the human safety zone and when moving close to the human, the robot moves at a speed that is slow enough to raise no risk;
The users shows first the assembly order.
Authors: Zhujun Zhang, Gaoliang Peng, Weitian Wang, Yi Chen, Yunyi Jia, Shaohui Liu
Publisher: Sensors
Year: 2022

## Slide 5: Fostering short-term human anticipatory behavior in human-robot collaboration
Tried to foster human anticipatory behaviour towards the robot, through visual cues of the robot’s next move;
The user has more trust in the robot and therefore the task completion time is decreased;
The testing remained limited to VR;
The user movement was detected using wearables.
Authors: Loizos Psarakis, Dimitris Nathanael, Nicolas Marmaras
Publisher: International Journal of Industrial Ergonomics
Year: 2022

## Slide 6: Social Cobots: Anticipatory Decision-Making for Collaborative Robots Incorporating Unexpected Human Behaviors
The objective is to handle unexpected conditions:
  when the human’s intention is estimated to be irrelevant to the assigned task and may be unknown to the robot, e.g., motivation is lost, another assignment is received, onset of tiredness;
  when the human’s intention is relevant but the human doesn’t want the robot’s assistance in the given context, e.g., because of the human’s changing emotional states or the human’s task-relevant distrust for the robot;
Partially observable Markov decision process (POMDP);
Tested in Simulation.
Authors: Görür O., Rosman B., Sivrikaya F., Albayrak S.
Publisher: ACM/IEEE International Conference on Human-Robot Interaction
Year: 2018

## Slide 7: Summary
Data Sources | Supervised Learning | Supervised Learning | Unsupervised Learning | Reinforcement Learning | OThers
RGB/RGBD images: pose, gaze, hand gestures, emotions, object information Voice commands Accelerometry Muscular Activity Sensor Fusion | Nearest Neighbor | Recurrent Neural Networks such as LSTM Convolution Neural Networks (CNN) Nearest Neighbor SVM Decision Trees Naive Bayes | Gaussian Mixture model (GMM) Hidden Markov model (HMM) Variational Autoencoder (VAE) | Q-learning SARSA Markov decision processes (MDP) | Look-up table of assembly sequences Open Pose
Lorem ipsum et tula lorem ipsum et lorem ipsum Lorem ipsum et tula lorem ipsum et lorem ipsum |  |  | Lorem ipsum et tula lorem ipsum et lorem ipsum | Lorem ipsum et tula lorem ipsum et lorem ipsum | 
Lorem ipsum et tula lorem ipsum et lorem ipsum | Lorem ipsum et tula lorem ipsum et lorem ipsum |  | Lorem ipsum et tula lorem ipsum et lorem ipsum | Lorem ipsum et tula lorem ipsum et lorem ipsum |